## Slide 1: Rescue Radar™

## Slide 2: Agenda
Rescue Radar Operation Overview
Questions

## Slide 3: RESCUE RADAR
What is Rescue Radar?
Notes: Introducing Conquest – for a keen eye in concrete imaging

## Slide 4
Designed for Search and Rescue
Safe, quick, easy to use
Rapid on-site results
What is Rescue Radar?

## Slide 5
Victim detection through rubble and solid material
Triangulation through grid-like survey
Time-Lapse mode allows monitoring of known victims
What is Rescue Radar?

## Slide 6
Rescue Radar Deployment
Operator stands > 50 feet away so their movement is not detected.

## Slide 7
Simple Operation

## Slide 8
Quick Results

## Slide 9: Rescue Radar Components
Battery
NIC-500R

## Slide 10
Built in GPS receiver for geotagging of results
75m Wi-Fi Range
Rechargeable battery
Built-in transport and protective weatherproof case
Rescue Radar Components
3rd Generation
Rescue Radar System

## Slide 11: Rescue Radar Interface

## Slide 12
Same layout with added features that are easily accessible
Home Screen

## Slide 13
Basic Mode
Displays a single reading and refreshes after a set cycle length
Mode

## Slide 14
Toggle between the material (Air, Snow, Rubble or Soil) being scanned with preset velocities for accurate depth to target
Material
Notes: Tog

## Slide 15
Adjust the depth range that is displayed on the screen during data collection or playback
Depth

## Slide 16
Adjust the Sensitivity level from 1 to 6 on the fly during data collection or playback depending on your requirements
Sensitivity

## Slide 17
Time Lapse Mode
Displays up to 10 consecutive readings at once taken a set cycle length
Mode

## Slide 18: Practical Considerations
Ground Coupling
  Ensure that the radar unit is well seated to ensure maximum signal
  Do not place on exposed metal
  Ensure radar unit will not move during data collection

## Slide 19: Practical Considerations
Good Penetration
Poor Penetration
Materials
Air
Wood
Snow
Sand
Soil
Non-reinforced concrete
Mixed rubble
Reinforced concrete
Clay Soil
Heavily reinforced concrete
Mixed rubble with large quantities of metal

## Slide 20: Practical Considerations
Sensitivity Setting
Multiple sensitivity levels are available to optimize data in individual circumstances
Easiest set in Time Lapse mode
A low sensitivity may not show any targets, while a high sensitivity may show false positives

## Slide 21: Practical Considerations
Survey Type
Collect data either in a structured grid survey, or in individual targeted location
Targeted scans can give quick results at sites that have been determined to be more likely of interest

## Slide 22: Practical Considerations
Grid Survey:
In this method, Rescue Radar is used to probe for movement in a regular pattern, typically with 5 meters between locations

## Slide 23: Limitations
GPR cannot penetrate metal, making heavily reinforced material difficult to survey
Depth is approximate, based on the selected material type
False positives can occur, especially if rescuers or objects are moving within a 15 meter radius

## Slide 24: Benefits
Can be deployed within minutes
Safe!
Uses radio waves similar to FM radio stations
Operate in a wide variety of environments
Non-destructive

## Slide 25: Questions?